## Slide 1
Introduction to Embedded and Robotics Programming
Cosmin Bonchis, Alin Brindusescu, Theodor Grumeza
Notes: *** Version of 2017 ***
1

## Slide 2
Introduction to Embedded and Robotics Programming
Lector Dr. Cosmin Bonchiș
Affiliations:
  West University of Timisora
Contact: cosmin.bonchis@e-uvt.ro
Dipl. Ing. Alin Brîndușescu
Affiliations:
  Elektrobit
  West University of Timisora
Contact: alin.brindusescu77@e-uvt.ro
Theodor Grumeza
Affiliations:
  West University of Timisora
Contact: theodor.grumeza@e-uvt.ro

## Slide 3
Introduction to Embedded and Robotics Programming
Course Objectives
Develop the minimum necessary skill for reading an electronic circuit
Discuss major components of an embedded system
Solve well defined problems on an embedded platform
Get familiar with tools used for embedded development
Understand the basic building blocks of a robotic system
© University of West & Elektrobit (EB) 2018
3

## Slide 4
Introduction to Embedded and Robotics Programming
Learning Outcomes
Learn how to read and replicate a simple electronic circuit
Understand what is a microcontroller and an embedded system
Become familiar with embedded programming environment
Understand key concepts of embedded systems: I/O, timers, interrupts, etc.
Learn embedded systems debugging techniques
Understand what are robots and the building block of a robotic system
Apply the embedded programming skills for driving a small robotic system
© University of West & Elektrobit (EB) 2018
4

## Slide 5
Introduction to Embedded and Robotics Programming
Course Structure
W1: Introduction and …
W2: W3: W4: EMBEDDED C …
W5:Basic Electronics II, Microcontroller Architecture
W6: I/O module , Interruptions
W7: Analog to Digital Converter, Robotics Basics
W8: Actuators and Drivers
W9-W13: Project
W14: Project presentation
© University of West & Elektrobit (EB) 2018
5

## Slide 6
Introduction to Embedded and Robotics Programming
Course Structure
Weekly laboratory class – 3 Working Groups
  W2 - W9
    30 minutes theoretical presentation
    1 hour experiments
  W10 – W 13
    Project work
  W14
    Project presentation
© University of West & Elektrobit (EB) 2018
6

## Slide 7
Introduction to Embedded and Robotics Programming
Grades
Mandatory requirement for both teams: own github.com or bitbucket.com account with all the code from laboratory committed
© University of West & Elektrobit (EB) 2018
7
Blue team
  no class presence required
  exam from the theory material provided in week 7
  max grade 7
Green team:
  class presence and involvement required
  based on the evaluation of the final project from week 14.
How to fail the exam:
  Chose the green team and come to the class and disturb your colleagues who want to experiment more

## Slide 8
Introduction to Embedded and Robotics Programming
Laboratory Experiments and Project
Based on Arduino Uno R3
© University of West & Elektrobit (EB) 2018
8
Plenty of peripherals available
Robotics Kit

## Slide 9
Introduction to Embedded and Robotics Programming
Project Ideas
Robotics
  Drive the robotic platform trough the environment using ultrasound sensors
IoT
  Door opening counter with digital display
  Windows breaking alarm
  Digital thermometer
Open for suggestions
© University of West & Elektrobit (EB) 2018
9

## Slide 10
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
© University of West & Elektrobit (EB) 2018
10

## Slide 11
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
© University of West & Elektrobit (EB) 2018
11
Electric current
  Flow of electric charge
  Symbol: I
  Ampere (A) as measuring unit
  Measurement tool: Ammeter, Galvanometer, rom: Ampermetru
Notes: All our electric and electronic circuits need electric current to function. The electric current is the flow of the electric charge.
Because electricity is abstract and it can not be so easy visualized you can imagine the flow of electrons as the water flowing through the pipes.
Example with the notation of the current and explain that if the value of I is negative basically the current flows in the opposite direction
11

## Slide 12
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Type of electric current: AC - alternative current
© University of West & Elektrobit (EB) 2018
12

## Slide 13
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Type of electric current: DC - direct current
© University of West & Elektrobit (EB) 2018
13

## Slide 14
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Where do we have AC and where DC?
© University of West & Elektrobit (EB) 2018
14
What type of electric current are using our gadgets?

## Slide 15
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Voltage
  Potential difference
  Pressure to push the electrons to move
  Symbol: U
  Volt (V) as measuring unit
  Measurement tool: Voltmeter, Galvanometer, rom: Ampermetru
© University of West & Elektrobit (EB) 2018
15
Notes: The voltage between two points is equal to the work done per unit of charge against a static electric field to move a test charge between two points.
Voltage/potential difference can be compared to water stored in a tank. The larger the tank, and the greater its height (and thus its potential velocity), the greater the water’s capacity to create an impact when a valve is opened and the water (like electrons) can flow.
15

## Slide 16
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
© University of West & Elektrobit (EB) 2018
16
Notes: Why not a direct line between the 2 electrodes? Because electric current is finding the path with less resistance (lazy path).
16

## Slide 17
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Ohm’s Law
  Current flowing through a conductor is directly proportional with the voltage
  Resistance (R) – the constant of proportionality – measured in ohms (Ω)
© University of West & Elektrobit (EB) 2018
17
Notes: It is an empirical law, the form we are using is a reformulation made by Kirchhoff. It will not always hold: Any given material will break down under a strong-enough electric field, and some materials of interest in electrical engineering are "non-ohmic" under weak fields.
Temperature has also an effect since the resistance is temperature dependent.
Looking from the point of view of the energy source any circuit can be reduced to this simple form.
17

## Slide 18
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Resistors
  Passive components that are obeying Ohm’s law
  Designed to have a specific resistance value R
  Common usage: reduce current flow, divide voltages, terminate transmission lines, …
© University of West & Elektrobit (EB) 2018
18
Notes: Rheostat are basically potentiometers for higher currents. Rheostats were often used as power control devices, for example to control light intensity (dimmer), speed of motors, heaters and ovens. Nowadays they are not used for this function anymore. This is because of their relatively low efficiency.
18

## Slide 19
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
© University of West & Elektrobit (EB) 2018
19
Example 1:
Example 2:
Notes: E1: 120 KO, 5% tolerance
E2: 130 O, 1% tolerance
19

## Slide 20
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Serial circuit of Resistors
© University of West & Elektrobit (EB) 2018
20
+ ... +

## Slide 21
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Parallel circuit of Resistors
© University of West & Elektrobit (EB) 2018
21
+ ... +

## Slide 22
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
Resistor networks
© University of West & Elektrobit (EB) 2018
22
R1+R2+R3||(R4+R5+R6||(R7+R8+R9))
Notes: R1+R2+R3||(R4+R5+R6||(R7+R8+R9)).
22

## Slide 23
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
How to use a multimeter: Measuring Voltage
© University of West & Elektrobit (EB) 2018
23

## Slide 24
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
How to use a multimeter: Measuring Current Intensity
© University of West & Elektrobit (EB) 2018
24

## Slide 25
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
How to use a multimeter: Measuring Resistors
© University of West & Elektrobit (EB) 2018
25

## Slide 26
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
How to use a multimeter:
  Always remember:
    voltage in parallel, current intensity in series
    don’t measure the other elements (resistors, diodes) when under power
© University of West & Elektrobit (EB) 2018
26
Notes: 26

## Slide 27
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
More to read:
  https://kaiserscience.wordpress.com/physics/electromagnetism/electric-current/
  https://learn.sparkfun.com/tutorials/resistors
  https://learn.sparkfun.com/tutorials/how-to-use-a-multimeter
© University of West & Elektrobit (EB) 2018
27

## Slide 28
Introduction to Embedded and Robotics Programming
Basic Electronics For Programmers
© University of West & Elektrobit (EB) 2018
28
Happy Hacking!
C U next Week!